## Slide 1
Teterboro Users Group
July 17th , 2013
Teterboro Issues
Safety by Design

## Slide 2
Jaike 3 Arrival….. Busting altitude restrictions……

## Slide 3
NBAA:
New York Metro Airspace Overview
JAIKE Three RNAV STAR
July 6, 2012
The JAIKE RNAV STAR serves arrivals into Teterboro, NJ (TEB) and Morristown, NJ (MMU) airports. These RNAV STARs are specifically designed to take advantage of the lateral and vertical navigation capabilities of today’s modern RNAV-equipped aircraft.
The complexities of the Northeast US terminal airspace necessitate airplanes entering and exiting airspace boundaries at specific points and altitudes. The JAIKE Three’s vertical descent profile is design to separate inbound TEB & MMU arrival traffic with other New York arrival traffic passing overhead and with Philadelphia departure traffic passing beneath. The vertical separation requirements between these flows within this area are very tight.
During a recent controller shift, 4 out of 7 airplanes (57%) failed to comply with the “at” 13,000 restriction at ILENE (i.e. descended early after passing JAIKE at 13,000’. This is an unacceptably high pilot deviation rate for this procedure.

## Slide 4
In a Falcon EASy Cockpit we can “see” the restrictions and our Path…..
Top of Descent after ILENE

## Slide 6
Check on the Honeywell Portal for these types of issues

## Slide 7
Localizer and Glide Slope Issues

## Slide 8
If I hear “Cleared for the Approach” should I always hit the APP button??
Once you’ve “armed” the approach, you’re telling the system to capture the localizer and glide slope whenever it can…. Ready or not….
Automation can bite you sometimes
Nav to Nav Pre-select

## Slide 9: Hitting the APP button too soon – example #1 KTEB ILS 6
Falcon xxx, cross DANDY at 1500’ cleared for the ILS 6 approach at Teterboro
x

## Slide 10
False Localizer Capture
Example 2: Hitting the APP button too soon

## Slide 11: Conclusion: Don’t push APP button until within ~ 80 of Inbound Loc Course

## Slide 12
We had a complaint about a Falcon … they were complaining the ILS capture didn’t work correctly…. Full scale deflections on downwind…. ????
The Help Desk had a Falcon that claimed his ILS didn’t work correctly at KTEB

## Slide 13
How does the ILS (Instrument Landing System) work ??
Two Antennas Used

## Slide 14: Remember the old, old A-N radio range?
1944 chart
On course with equal “amounts” of A & N

## Slide 15: Rather than A – N, the ILS works with 90 Hz – 150 Hz
The Glide Slope turns the antenna on it’s side and bounces the beams off the ground
The Localizer antenna is centered on the runway but beyond the end ….
If more 90 Hz than 150 Hz… fly right to center
Why?
If more 90 Hz fly down, more 150 Hz go up

## Slide 16: False Glide Slopes
False signals may be generated along the glide slope in multiples of the glide path angle, the first being approximately 6º degrees above horizontal. This false signal will be a reciprocal signal (i.e. the fly up and fly down commands will be reversed). The false signal at 9º will be oriented in the same manner as the true glide slope. There are no false signals below the actual slope. An aircraft flying according to the published approach procedure on a front course ILS should not encounter these false signals.
This is because of a radiation pattern of the antenna and the ground reflection of some of the transmitted energy, resulting in more than one overlapping lobe.

## Slide 17: How low can you follow the GS ?
NOTE- Unless otherwise coordinated through Flight Standards, ILS signals to Category I runways are not flight inspected below 100 feet AGL. Guidance signal anomalies may be encountered below this altitude.
Caution about following the GS !
GS Antenna
250’ – 650’
TCH: 50’
100’ AGL
200’

## Slide 18: Did you ever see this type of warning ? AP NA with about 400’ to go
960’-576’= 384’

## Slide 19: What’s the issue here: KMMU ILS 23
627’ – 384’ = 243’ to go
Notam:

## Slide 21: KMMU Critical Area not “smooth” and is on a swamp!
GS Antenna

## Slide 22: Check Notams: Snow Banks deflecting GS Beam

## Slide 23
Issue with KTEB ILS 19

## Slide 24
GS
Unexpected Consequences
Teterboro Airport- Taxiway Q Expansion
GS

## Slide 25
Glide Slope antenna uses ground to bounce half of the signals up
But what if reflected portion is blocked ?

## Slide 26
Taxi Q
G/S 19
Taxiway Q Interference for ILS 19 Glide Slope

## Slide 27
Normal Glide Slope – Intercept from below
Loc Captured GS Armed
G/S Captured
On Loc and G/S
Airplane blocks signal- receiver thinks its’ on GS- ALT mode goes to GS
Blocking airplane moves away… now in loc/gs, airplane sees glide slope above pitches up to recapture….

## Slide 28
Interference issue with the ILS 19 at Teterboro

## Slide 29
1-1-9k-2b Weather Conditions. At or above ceiling 800 feet and/or visibility 2 miles.
(1) No critical area protective action is provided under these conditions.
(2) A flight crew, under these conditions, should advise the tower that it will conduct an AUTOLAND or COUPLED approach to ensure that the ILS critical areas are protected when the aircraft is inside the ILS MM.
Pilots are cautioned that vehicular traffic not subject to ATC may cause momentary deviation to ILS course or glide slope signals. Also, critical areas are not protected at uncontrolled airports or at airports with an operating control tower when weather or visibility conditions are above those requiring protective measures. Aircraft conducting coupled or autoland operations should be especially alert in monitoring automatic flight control systems.
AIM Caution on ILS in VMC

## Slide 30
..Further RADAR analysis showed that even if the WX was below 800 and 2 the critical area at the time of anomaly would not have been protected. The aircraft was well outside TUGGZ and there was no one on the approach ahead, inside of TUGGZ.
Issue exists even in IMC !
ATC is only required to protect the ILS Critical Area from the FAF inbound. This issue occurs not only at KTEB but at KLGA and many other airports around the country.

## Slide 31
Jepp can put a warning on the chart
Jepp.
Gov.
Doesn’t seem like the Government charts do the same….

## Slide 32
How to fly the ILS 19 Knowing this issue ??
Maybe stay in LNAV until TUGGZ …. Then hit APP
Or…. Wait for an LPV approach to 19

## Slide 33
TO mode is de-selected when a new vertical mode is selected, when the crew
members manually change the vertical guidance mode, or automatically if the airplane
reaches the ASEL………. OR……. When the vertical mode leaves TO for ASEL capture…..
A/T Auto mode issue on departures at KTEB

## Slide 34
Woody Saland, PhD
Director, Avionics Programs and Pilot Training
Safety by Design
The Falcon EASy Flightdeck

## Slide 35
Today let’s talk about three issues in flying:
1. Crew CRM
(how to work together as a team)
2. Flying Blind - Seeing your trajectory
(path / track vs. pitch / heading)
3. Situational Awareness
(where am I ?)

## Slide 36: CRM: Cockpit Resource Management
Flying is hard enough, but getting rid of the left seat master Captain mentality was tougher…. CRM is about …. How do you get two pilots to work together as a team
August 2012 NCBAA

## Slide 37
CRM and VNAV in the Olde Days
The problem is how to introduce something new without re-training

## Slide 38: The Issue: The cost to re-train a pilot

## Slide 39: The EASy Philosophy
Shared Displays
Strategic Information
Tactical Information.
Tactical Information

## Slide 40: Deliberately Limited Display Options
ADI
HSI
ENG
CAS
ADI
HSI
ENG
CAS
ECL
Electronic Checklist
Sharing the center allows both pilots to be on the same “page” and to work together by design not by edict

## Slide 41
Common, Strategic items are handled together as a team
CRM by Design

## Slide 42
No other flightdeck has the crew working together in the middle on shared tasks….
every other company has left / right sides to the cockpit
Falcons

## Slide 43
Here’s the two latest airline flightdecks…. Note the duplication of map / double cue flight directors
Airbus A380
Boeing B787 Dreamliner
Two sides to the flight deck…. Not common ground in the middle

## Slide 44
Flying Blind
Pitch/Hdg vs. Path/Track
The Skill of Instrument Flying

## Slide 45
Interpreting your Instruments

## Slide 46: Up until 1929, no instrument flying
Charles Lindbergh’s flight to Paris: May 20–21, 1927
August 2012 NCBAA

## Slide 47: September 24th, 1929 Jimmy Doolittle Proves you can fly “blind”
Sperry Gyroscope Company, developed what is now called an "attitude indicator.“
NY-2 airplane- Mitchell Field, NY
Airplane Centric: No one instrument to show your relationship with the ground

## Slide 48: Since 1929, most airplanes fly “instruments” using pitch and heading
The more or less standard
“6 pack” of flight instruments
Most “glass” cockpits duplicate the
“6 pack” round dial concept

## Slide 49: The Problem ? Not only was this not “easy”, but a good scan takes work and practice

## Slide 50
No wonder pilots need to constantly practice their “instrument scan”
Using a simulator, researchers at the University of Illinois conducted a study with 20 pilots who had no instrument training to see the survivability of an encounter with IMC conditions. All of them lost control, and the only variable was how long it took. The range was as short as 20 seconds to as long as 480 seconds with the average being 178 seconds.
There needs to be a better way to fly…. And there is: PATH not Pitch

## Slide 51
We don’t really care where the nose is pointed (pitch & heading) we care about the trajectory (path and track) … we now have the tools to show that to a pilot…. It started with the military…..
Our goal in flying is to fly a certain trajectory, regardless of the wind or conditions

## Slide 52
The use of Side Stick Fly by Wire, Head’s Up Displays and Moving Maps has been well proven by years of experience in the Mirage and Rafale fighters..
Rafale Cockpit
F7X SideStick
Dassault is the only Business Jet manufacturer to build military jets side by side
The Value of a Heads’ Up Display

## Slide 53: Why not fly by PATH…. Like a HUD
Aircraft Symbol
Fixed in center
Flight Path Symbol
Flight Director
Acceleration
Chevron

## Slide 54
The EASy cockpit revolutionized business Jet flightdecks with the integration of Heads Up technologies with Flight Deck displays….
1st Generation EASy
EASy II with Synthetic Vision

## Slide 55: We now have a day time HUD like view for both pilots…. No more flying “blind”

## Slide 56
Small x-wind, HDG centered … like HUD
With Path I can see where I’m going

## Slide 57: Visualizing the Vertical Trajectory
Flying an approach with Path, both pilots see the trajectory

## Slide 58
New B787 Dreamliner
Falcon EASy II
Contrast EASy with a traditional flight director in the latest Boeing Dreamliner…..

## Slide 59
Situational Awareness is giving pilots the vision to see where they are and where they are going……
Let’s look at three CFIT* accidents…..
* CFIT: Controlled Flight Into Terrain….. That is, flying a perfectly good airplane into a mountain
Oct. 24th, 2004
Dec. 20th, 1995
May 9th , 2012
Cali
Hendrick
Sukhoi Superjet

## Slide 60
Cali
Airport
Crash site
Crew was unaware
they were descending
into the mountains
with their
airbrakes on !
American Airlines B757
Cali, Columbia

## Slide 61
EASy: better visualization tools
B757
EASy

## Slide 62: Hendrick Racing Crash (10-24-04)
1981 Beech 200 King Air
10 Fatalities
The crew improperly read instruments and missed a landing approach to Blue Ridge Airport in Martinsville, Va., the NTSB said in a report synopsis e-mailed to The Associated Press. The Beech King Air 200 crashed into fog-shrouded Bull Mountain in the foothills of the Appalachians on Oct. 24, 2004.

## Slide 63
With Terrain Alert:
ADI: Pull Up
Audible “Pull Up Terrain”
Pop Up of 1/6 Terrain Window on Pilot Flying
Main I-Nav map converts to HDG Up and shows Interactive Terrain “flashing”
EASy CFIT Avoidance

## Slide 64: May 9th, 2012 Sukhoi Superjet 100 Crash Jakarta, Indonesia
2,211 m (7,254 ft)
Salak Volcano

## Slide 65
This is the captain and flightdeck of the airplane that crashed…. Where’s the big picture map showing the terrain or trajectory ?

## Slide 66
EASy gives a complete picture of the outside world– Heading Up, either along the flightplan route or straight ahead of the plane - Automatically
The Sukhoi accident was similar to the Cali crash….. Only 17 years later… with a brand new design that was / is to be the future of Russian Commercial Jets…
It’s hard to believe you could have a CFIT in a Falcon !

## Slide 67
And finally some illustrations of lack of situational awareness:
an accident involving taking off on the wrong runway
and three cases of landing on the wrong runway….

## Slide 68
Comair Flight 5191- August 2006
Acknowledged Runway 22, departed Runway 27
Only 1 survived, (FO lost leg, brain damage), 47 Pax and 2 out of 3 crew died
CRJ-100ER

## Slide 69
July 20th, 2012: Air Force officials are trying to figure out why an Air Force C-17 Globemaster III cargo jet heading to MacDill Air Force Base instead landed at Peter O. Knight Airport this afternoon.
This is the second time this has happened," said spectator Gary Garrett, 71, who has a real estate office on Davis Islands. "The last time, it was a 727 in the 80s," he recalled, "and they took that plane apart to get it out of here."
3,500’ long
11,500’ long

## Slide 70
August 9,2012

## Slide 71
Oct. 28th, 2006: The National Transportation Safety Board is investigating the landing of Continental Flight 1883, which was carrying 154 people from Orlando, Fla. Both pilots were grounded by the airline.
"Being cleared to land on a different runway than the one you are flying the approach to introduces a whole new set of complexities to the pilots at a very critical time, especially when the landing runway does not have a precision approach," said Capt. Denis Breslin, an American Airlines pilot and spokesman for the Allied Pilots Association, the airline pilots union. "Trying to make those decisions in dusk or poor visibility without benefit of course guidance increases the chance for error," he added.
ILS 22L

## Slide 72
Safety by Design – Showing the Pilots where they are !

## Slide 73
Questions ?